# Preliminaries
To run PyPar3 as Gtk-Application you need a class Application like this in pypar3.py. This class defines textdomain, bindings and locales and controls startup:
def do_startup(self):
Gtk.Application.do_startup(self)
#gettext.textdomain doesn't work with the GTK3 glade files
locale.bindtextdomain(consts.appNameShort, consts.dirLoc)
locale.textdomain(consts.appNameShort)
#gettext.textdomain(consts.appNameShort)
#gettext.bindtextdomain(consts.appNameShort, consts.dirLoc)

In module consts.py all parameters are defined.

In all python modules with translatable strings we must include gettext:
from gettext import gettext as _
The text for translation must be wrapped as
text = _('string to translate')
The following description presumes that the project has at least 3 directories at same level:
locale/de_DE/LC_MESSAGES/myapp.mo
po
src
res
src contains the python source files
res contains the glade graphical interfaces
po will receive the pypar3.pot file including the extracted strings
locale will recive the translations
The dir structure locale/….. is required by gettext:
Because many different languages for many different packages have to be stored we need some way to add these information to file message catalog files. The way usually used in Unix environments is have this
encoding in the file name. This is also done here. The directory name given in ‘bindtextdomain’s second argument (or the default directory), followed by the name of the locale, the locale category, and the domain name are concatenated:
DIR_NAME/LOCALE/LC_CATEGORY/DOMAIN_NAME.mo
The default value for DIR_NAME is system specific. For the GNU library, and for packages adhering to its conventions, it’s: /usr/local/share/locale
LOCALE is the name of the locale category which is designated by ‘LC_CATEGORY’. For ‘gettext’ and ‘dgettext’ this ‘LC_CATEGORY’ is always ‘LC_MESSAGES’.(1) The name of the locale category is determined through ‘setlocale (LC_CATEGORY, NULL)’. (2) When using the function ‘dcgettext’, you can specify the locale category through the third argument.
For packaging we can handle DIR_NAME for instance optimized for DEBIAN package or in a different suitable way for packaging in SNAP.
The part below DIR_NAME is given to local/lang/LC_MESSAGES/pypar3.mo since gettext expects this.

# Create translation files
## Extract strings with xgettext
With the xgettext tool you can extract all translatable strings from the python source code, store them in a PO template file with file extension .pot. Don't edit the POT file - xgettext overwrites it each time you start it.
xgettext -j -o ./po/pypar3.pot ./src/pypar3.py
Do this for all python files appending texts to the pypar3.pot file.
If your project includes graphical interfaces generated by glade you can extract the texts with
xgettext -j --keyword=translatable -o ./po/pypar3.pot ./res/win-main.glade
Do this for all glade files appending texts to the pypar3.pot file.

## Create initial PO files with msginit
If your translations contains non-ASCII characters, change the charset in the header from ASCII to UTF-8:
"Content-Type: text/plain; charset=UTF-8\n"
In the initial step when we have to create the PO files the first time, we can use msginit.
msginit --locale de --input pypar3.pot --output locale/de/LC_MESSAGES/pypar3.po
msginit --locale fr --input pypar3.pot --output locale/de/LC_MESSAGES/pypar3.po
As msginit overwrites an existing PO file, you shouldn't call it if you have already PO files containing translations. In this case use msgmerge as described later.
The POT file is the template file used to create a new PO file for each target language. Place them in directories as mentioned above. You can do this also manually.

## Managing changes with msgmerge and translate the PO files
If you're updating your code, you might change translatable texts, too. This requires an update of the PO/MO files. There's, of course, a gettext tool to simplify this task, it's called msgmerge. First, you have to extract the translatable strings from the new sources using xgettext. This overwrites your old POT file with a new one. Then you can merge the changes into the language-specific PO files:
msgmerge --update de_DE.po pypar3.pot
This must be performed for each translation.
msgmerge doesn't delete any translation: If a string is no longer found in the source code, it is marked as deleted in the PO file:
#~ msgid "Draft"
#~ msgstr "Entwurf"
New strings are added to the PO file, for unchanged strings the source code line number, and the extracted comment are updated, if necessary.
msgmerge also tries to detect changed strings using a fuzzy string comparison. If only a small part of the string has changed the new string is saved together with the old translation in the PO file and the entry is marked as "fuzzy".
Now you can start translating the language specific PO files. You can use a text editor or a special translation editor for that.

## Convert PO to MO files using msgfmt
You next have to convert the PO files into "Message Object" files (with the extension .mo) in the appropriate localeDir:
msgfmt -v de_DE.po --output-file=../locale/de/LC_MESSAGES/pypar3.mo
This must be performed for each translated file.

Source:
https://www.codeandweb.com/babeledit/tutorials/translation-with-gettext-and-php